## Slide 1: ANALOG AND DIGITAL ELECTRONIC CONCEPTS, NUMBER SYSTEMS
Analog vs. Digital
Number Systems
Arithmetic Operations on Binary Numbers
One’s Complement and Two’s Complement
Signed Numbers

## Slide 2: Analog vs. Digital
There are two types of electronic circuits: Analog and digital circuits.
Analog signal is continuous. It means that, analog circuits process continuous values.
Digital signal is discrete (discontinuous). Digital circuits process discrete values.
Digital representation of data has advantages over analog representation, in terms of data processing, interpreting, storing, and transmission.
Time
Temperature
Time
Temperature

## Slide 3: Analog vs. Digital
A digital value is represented by a combination of ON and OFF voltage values. Generally, +5V is considered ON, and 0V is considered OFF.
For instance, the temperature value 25⁰C can be input to a digital circuit as a string that consists of ON and OFF values.
These voltage values are interpreted as logic 1’s and 0’s, and can be represented as “11001” in binary system.

## Slide 4: Number Systems
Decimal System (Base 10)
This is the system we use in our daily life. The digits from 0 to 9 is used to represent 10 different values.
123.456
Weights of corresponding digits are: 102 101 100 . 10-1 10-2 10-3
The decimal number 123.456 denotes
(1×102)+(2×101)+(3×100)+(4×10-1)+(5×10-2)+(6× 10-3)

## Slide 5: Number Systems
Binary System (Base 2): In binary system, only the symbols 0 and 1 are used to represent the numbers. 0’s and 1’s are called bits.
In binary numbers, the rightmost bit is called LSB (Least Significant Bit), and the leftmost bit is called MSB (Most Significant Bit).
110010012
MSB LSB
An n-bit binary number can be between 0 and (2n -1).
110.0112
Weights of corresponding bits are: 22 21 20 . 2-1 2-2 2-3

## Slide 6: Number Systems
Conversion of binary numbers to decimal:
Binary numbers are converted to decimal by adding up the weights of 1’s.
The binary number 101102 corresponds to decimal number 24+22+21=22
In other words;
(10110)2 = (22)10
The binary number 10.1012 corresponds to decimal 21+2-1+2-3 = 2.625

## Slide 7: Number Systems
Conversion of decimal numbers to binary:
This conversion can be done in two ways.
1st method
Write down the binary weights as a sequence as below. (The number of bits depends on the number to convert).
… 256 128 64 32 16 8 4 2 1
Then, find out which weights have a sum of the number to convert. And then, mark those bits as 1, and the rest as 0.
Example: Let’s convert 98 to binary.
98 = 64 + 32 + 2
So, we find out that the binary number is;
64 32 16 8 4 2 1
( 1 1 0 0 0 1 0 )2
This method is practical especially when converting smaller numbers.

## Slide 8: Number Systems
Conversion of decimal numbers to binary:
2nd method
To convert a decimal number to binary, we divide the decimal number by 2 consecutively until the quotient is 0, and take the remainders.
The remainder of first division is the LSB, and the remainder of last division is MSB.
Example: Let’s convert (13)10 to binary.
Division Remainder
13/2 = 6 1 (LSB)
6/2= 3 0 (13)10 = (1101)2
3/2= 1 1
1/2= 0 1 (MSB)

## Slide 9: Number Systems
Conversion of decimal floating point numbers to binary:
This conversion can be done in two ways.
1st method
Write down the weights of fractional part of the floating point number as a sequence below.
0.5 0.25 0.125 0.0625 …
Then, find out which weights have a sum of the fractional part to convert. And then, mark those bits as 1, and the rest as 0.
Example: Let’s convert (0.625)10 to binary.
0.5 0.25 0.125 …
( 1 0 1 )2
So, (0.625)10 = (0.101)2

## Slide 10: Number Systems
Conversion of decimal floating point numbers to binary:
2nd method
Multiply the fractional part by 2 consecutively until the fractional part of the result is 0, or until we decide that we have enough bits.
Then, we get the whole parts of the results.
Example: Let’s convert (0.625)10 to binary.
0.625×2 = 1.25 (MSB)
0.25×2 = 0.50 (0.625)10=(0.101)2
0.5×2 = 1.00 (LSB)
The fractional part is 0.
It means that the conversion is done.

## Slide 11: Arithmetic Operations on Binary Numbers
Binary Addition
Binary addition has 4 basic rules:
0 + 0 = 0, 0 + 1 = 1, 1 + 0 = 1, 1 + 1 = 10 (0 carry 1)
If we also have a carry bit to add, there are 4 different probabilities.
Carry Sum
Carry
1 + 0 + 0 = 01
1 + 0 + 1 = 10
1 + 1 + 0 = 10
1 + 1 + 1 = 11
Example:
1012
+ 0012
1102

## Slide 12: Arithmetic Operations on Binary Numbers
Binary Subtraction
Binary subtraction has 4 basic rules.
0 - 0 = 0, 1 - 0 = 1, 1 - 1 = 0, 10 - 1 = 1 (We borrow 1 from the left bit)
Example:
Binary Multiplication
Binary multiplication has 4 basic rules
0 × 0 = 0, 0 × 1 = 0, 1 × 0 = 0, 1 × 1 = 1
It is similar to decimal multiplication.

## Slide 13: Arithmetic Operations on Binary Numbers
Example:
Binary Division
This operation is also similar to decimal division.
Example:
Partial
products

## Slide 14: One’s Complement and Two’s Complement
One’s complement and two’s complement are especially used in representing negative numbers and performing arithmetic operations on negative numbers.
One’s complement
We calculate one’s complement by simply converting 1’s to 0’s and 0’s to 1’s.
Example:
We can also calculate one’s complement by the formula 2n-N-1 where n is the number of bits, and N is the binary number.
Example:
One’s complement of 1101102 is 26-110110-1=1000000-110110-1
=1000000-(110111) = 001001
Binary Number
One’s Complement

## Slide 15: One’s Complement and Two’s Complement
Two’s complement
We calculate two’s complement by simply adding 1 to one’s complement.
We can also calculate two’s complement by the formula 2n-N where n is the number of bits, and N is the binary number.
Example:
Two’s complement of 1101102 is 26-110110 = 1000000-110110
= 001010
Binary Number
One’s Complement
Two’s Complement

## Slide 16: Signed Numbers
Signed numbers contain both the sign and the magnitude. Sign is whether the number is positive or negative, and quantity is the value of the number. In binary system, signed numbers can be represented in three forms: Sign-Magnitude, One’s Complement, and Two’s Complement.
In all these three methods, if the MSB is 1, then the number is negative.
Sign-Magnitude Form
In sign-magnitude form, the MSB represents the sign, and the rest bits represent the magnitude.
The magnitude part is the value of the number, no matter what the sign is.
Example: Let’s convert (-19)10 and (19)10 to 8-bit binary.
-19 = (10010011)2 19 = (00010011)2
Sign bit
Magnitude bits
Sign bit
Magnitude bits

## Slide 17: Signed Numbers
One’s Complement Form
Positive numbers are represented just the same as sign-magnitude form. Negative numbers are represented as one’s complement of the magnitude.
Example: Assuming that we store the numbers in 8-bits, we represent the number -19 as one’s complement of +19 (00010011)2, which is (11101100)2.
Two’s Complement Form
Positive numbers are represented just the same as sign-magnitude form. Negative numbers are represented as two’s complement of the magnitude.
Example: Assuming that we store the numbers in 8-bits, we represent the number -19 as two’s complement of +19 (00010011)2, which is (11101101)2.

## Slide 18: Converting Signed Numbers to Decimal
If the number is in sign-magnitude form, we convert the magnitude part (excluding the sign bit) just like an unsigned number. And then, check the sign bit to detect whether the number is positive or negative.
Example: Let’s convert signed binary number 100110002 to decimal.
- (23+24)= - 24
If the number is in one’s complement form, we convert positive numbers just like an unsigned number. To convert negative numbers, we add negative weight of the sign bit to the sum of other bits’ weights, and then, add 1.
Example: 000110002 is a positive number because the sign bit is 0. So, the decimal value is 24+23=24.
Example: 111001112 is a negative number because the sign bit is 1. So, the decimal value is -27+26+25+22+21+20 + 1 = -24.

## Slide 19: Converting Signed Numbers to Decimal
If the number is in one’s complement form, we convert positive and negative numbers by adding negative weight of the sign bit to the sum of other bits’ weights.
With N bits, we can represent numbers between -2N-1 and (2N-1 -1) in two’s complement form.
Example: The number 010001012 in two’s complement form is 26+22+20=69 in decimal.
Example: The number 101110112 in two’s complement form is -27+25+24+23+21+20 = -69 in decimal.
Two’s complement form is used extensively because both negative and positive numbers can be converted the same way. However, in one’s complement form, positive and negative numbers are converted in different ways. Another reason is that the number 0 causes an ambiguity in one’s complement form because it can be represented in two different forms: 000000002 and 111111112.